## Slide 1: PCB Tracking with Image Processing Techniques
Image Processing Final Project
Colin King & Matthew Noseworthy

## Slide 2: Overview
Our project’s goal was to locate a PCB within an image frame, in various background and lighting conditions.
This presentation will walk through our algorithm and briefly explain why each technique is utilised

## Slide 3: The Algorithm
Let’s walk through the steps of the algorithm
1

## Slide 4: Histogram Equalization
Image is converted to YUV format
Histogram equalization performed on the Y channel, UV channels unaltered
Contrast enhanced without modifying hue

## Slide 5: RGB to HSV Conversion
Our aim is to threshold a range of hue as well as saturation/brightness. RGB won’t suffice.
HSV has three channels: Hue, Saturation, and Value

## Slide 6: Median Spatial Filter (Median Blur)
Reduces salt & pepper noise
Enhances thresholding performance

## Slide 7: Thresholding
The goal is to remove all pixels that aren’t the PCB
Hue: 65-84 - removes everything except green
Saturation/Value: 70-255 – removes dark extrema

## Slide 8: Double Morphological Operation
Closing first: Fills gaps in green region where components are on the board
Opening second: Eliminate environmental noise that passes through thresholding

## Slide 9: HSV to Grayscale
The HSV image still has distinct regions of hue difference that are detected as edges by Canny
Converting to grayscale reduces this effect

## Slide 10: Canny Edge Detection
Frame contains only pixels from the PCB
Used industry standard sigma=0.33
Hysteresis Thresholds:
  int(max(0, (1.0 + sigma) * v)) -> int(max(0, (1.0 - sigma) * v))

## Slide 11: Contour Selection
Output from canny is a list of contours
For our application, we simply select the one with the largest area

## Slide 12: Demos
Pre-recorded video throughput & live video feed
2

## Slide 13
Place your screensot here
Video Demo
This demo runs a pre-recorded video of us moving a PCB around through the algorithm

## Slide 14
Place your screenshot here
Live Demo
This demo captures frames from a connected camera, and runs them through the algorithm

## Slide 15: References

## Slide 16: THANKS!
Any questions?